## Slide 1: Slide
What is Modulation?
Modulation is the process of varying a parameter of a high-frequency carrier signal according to a low-frequency information (message) signal, so that the information can be transmitted over a long distance efficiently.
The carrier signal is usually a high-frequency sinusoidal wave, and the message signal contains the actual information such as voice, music, data, or video.
In modulation, one parameter of the carrier wave is changed based on the message signal:
Amplitude
Frequency
Phase
The result is called a modulated signal.
Why Modulation is Necessary
Direct transmission of low-frequency message signals is not practical. Modulation solves several problems:
Increases communication range
High-frequency signals can travel longer distances with less loss.
Reduces antenna size
Antenna height is inversely proportional to frequency.
Higher frequency → smaller antenna.
Improves signal-to-noise ratio (SNR)
High-frequency transmission reduces the effect of noise.
Avoids signal mixing (interference)
Different users can transmit at different carrier frequencies.
Carrier Signal and Message Signal
Message Signal
Low frequency
Contains information
Cannot travel long distances efficiently
Example: human voice (20 Hz – 20 kHz)
Carrier Signal
High frequency
Does not contain information by itself
Used to carry the message signal
Example: radio frequency signals (MHz range)
Types of Modulation Techniques
Modulation techniques are mainly divided into two categories:
Analog Modulation
Digital Modulation
1. Analog Modulation
In Analog Modulation, both the carrier signal and the message signal are analog signals.
An analog signal is continuous in nature and can take infinite values between two limits.
Types of Analog Modulation
Amplitude Modulation (AM)
Amplitude of the carrier is varied
Frequency and phase remain constant
Frequency Modulation (FM)
Frequency of the carrier is varied
Amplitude remains constant
Phase Modulation (PM)
Phase of the carrier is varied
Amplitude and frequency remain constant
2. Digital Modulation
In Digital Modulation:
Carrier signal is analog
Message signal is digital (binary)
Digital modulation is widely used in modern communication systems such as mobile communication, Wi-Fi, and satellite communication.
Examples of Digital Modulation
ASK (Amplitude Shift Keying)
FSK (Frequency Shift Keying)
PSK (Phase Shift Keying)
QAM (Quadrature Amplitude Modulation)
Analog Waves
Analog waves are continuous signals.
They can take any value within a range
There are infinite possible amplitude levels
More sensitive to noise
Example:
Voice signal, temperature signal
Digital Signals
Digital signals are discrete signals.
They have only two levels:
Logic 0 → 0 volts
Logic 1 → non-zero voltage
No intermediate values exist
Less affected by noise
Example:
Binary data in computers
What are Digital Modulation Techniques?
Digital Modulation is the process of transmitting digital data (bits: 0 and 1) by modifying a high-frequency analog carrier signal.
Unlike Analog Modulation, where the carrier parameter changes continuously, in Digital Modulation the carrier parameter changes discretely between fixed values. This discrete
change is called Shift Keying.
Concept of Shift Keying
Shift Keying means:
The amplitude, frequency, or phase of the carrier signal is shifted between two or more fixed levels
Each level represents digital information (bits)
Because digital data is binary:
Two discrete levels are enough → Binary Shift Keying
More bits can be grouped together → M-ary Shift Keying
Types of Digital Modulation Techniques
There are three main types of Digital Modulation techniques:
Amplitude Shift Keying (ASK)
Frequency Shift Keying (FSK)
Phase Shift Keying (PSK)
1. Amplitude Shift Keying (ASK)
In ASK, the amplitude of the carrier signal is changed according to the digital data.
Frequency and phase remain constant
Amplitude switches between discrete levels
Binary ASK
Bit 1 → High amplitude
Bit 0 → Zero or low amplitude
Characteristics
Simple to implement
Highly affected by noise
Used in optical communication and RFID systems
2. Frequency Shift Keying (FSK)
In FSK, the frequency of the carrier signal is changed according to the digital data.
Amplitude remains constant
Two different frequencies are used
Binary FSK
Bit 1 → Frequency f₁
Bit 0 → Frequency f₂
Characteristics
Better noise immunity than ASK
Requires more bandwidth
Used in modems and low-speed data communication
3. Phase Shift Keying (PSK)
In PSK, the phase of the carrier signal is changed according to the digital data.
Amplitude and frequency remain constant
Phase switches between discrete values
Binary PSK (BPSK)
Bit 1 → Phase 0°
Bit 0 → Phase 180°
Characteristics
Very good noise immunity
More complex receiver
Widely used in modern communication systems
Comparison of ASK, FSK, and PSK
Amplitude Shift Keying (ASK)
Amplitude Shift Keying (ASK) is a digital modulation technique in which the amplitude of a high-frequency carrier wave is changed (shifted) according to the digital message signal, while the frequency and phase of the carrier remain constant.
Each digital symbol (bit or group of bits) is represented by a distinct amplitude level of the carrier wave.
Basic Principle of ASK
Digital data consists of discrete symbols
Each symbol is assigned a specific carrier amplitude
The carrier is transmitted only when required by the data
Hence, information is carried by amplitude variation only
Mathematically, the ASK signal can be written as:
where
= digital message signal (0 or 1, or M levels)
= carrier amplitude
= carrier frequency
= phase
Types of ASK
ASK is mainly divided into two types:
Binary Amplitude Shift Keying (Binary ASK)
M-ary Amplitude Shift Keying (M-ary ASK)
1. Binary Amplitude Shift Keying (Binary ASK)
In Binary ASK, one bit is transmitted at a time.
Logic 1 → carrier with a certain amplitude (for example, 12 V)
Logic 0 → carrier with zero or lower amplitude (often 0 V)
This special case where carrier is present for 1 and absent for 0 is also called
On–Off Keying (OOK).
Characteristics
Simple to generate and detect
Highly sensitive to noise
Poor power efficiency
2. M-ary Amplitude Shift Keying (M-ary ASK)
In M-ary ASK, a group of bits is transmitted as one symbol.
Number of bits per symbol =
Each symbol is assigned a unique amplitude level
Example: 16-ary ASK
Bits per symbol =
Total possible 4-bit combinations = 16
Therefore, 16 different amplitude levels are required
This increases data rate, but makes the system more sensitive to noise.
Coherent and Non-Coherent ASK
Coherent ASK
A single carrier wave is used
All amplitude levels are generated from the same carrier
Requires carrier phase synchronization at receiver
Better performance but higher complexity
Non-Coherent ASK
Multiple carriers with different amplitudes are used
No strict carrier phase synchronization needed
Simpler receiver but poorer performance
ASK Waveform Explanation
When :
Carrier appears with full amplitude
When :
Carrier amplitude becomes zero
Resulting waveform shows sudden amplitude changes
These abrupt changes increase bandwidth
Block Diagram of Amplitude Shift Keying (Transmitter)
Working of ASK Modulator
Analog Message → ADC
The analog message signal is converted into a digital signal using an Analog-to-Digital Converter (ADC).
Digital Signal m(t)
This digital signal represents logic 0s and 1s.
Carrier Generator
A high-frequency sine wave is generated:
Multiplier (Modulator)
The digital signal multiplies the carrier:
If , carrier passes
If , output becomes zero
Band-Pass Filter (BPF)
Removes unwanted frequency components and limits bandwidth
Output
The resulting signal is the ASK modulated wave
Demodulation of ASK (Receiver)
Working of ASK Demodulator
Received ASK Signal
The modulated signal is received from the channel.
Multiplier (Coherent Detection)
The received signal is multiplied by the same carrier frequency:
Low-Pass Filter (LPF)
Removes high-frequency components and extracts the baseband signal.
Recovered Digital Signal
The original digital message signal is obtained.
DAC (Optional)
If required, the digital signal is converted back into analog form using a Digital-to-Analog Converter.
Advantages of ASK
Simple modulation technique
Easy implementation
Low hardware complexity
Disadvantages of ASK
Highly sensitive to noise
Poor power efficiency
Requires higher bandwidth due to abrupt amplitude changes
Applications of ASK
Optical fiber communication
RFID systems
Infrared communication
Low-cost wireless systems
Frequency Shift Keying (FSK)
Frequency Shift Keying (FSK) is a digital modulation technique in which the frequency of a high-frequency carrier wave is changed (shifted) according to the digital message signal, while the amplitude and phase of the carrier remain constant.
Each digital symbol is represented by a different discrete frequency of the carrier wave.
Basic Principle of FSK
Digital data consists of symbols (bits or groups of bits)
Each symbol is assigned a unique carrier frequency
The carrier frequency switches between fixed values
Information is conveyed through frequency variation only
Mathematically, the FSK signal is written as:
where
= constant carrier amplitude
= carrier frequency corresponding to the symbol
= phase
Types of Frequency Shift Keying
FSK is mainly divided into two types:
Binary Frequency Shift Keying (Binary FSK)
M-ary Frequency Shift Keying (M-ary FSK)
1. Binary Frequency Shift Keying (Binary FSK)
In Binary FSK, one bit is transmitted at a time using two distinct frequencies.
Logic 1 → carrier frequency (e.g., 50 MHz)
Logic 0 → carrier frequency (e.g., 25 MHz)
Only the frequency changes; amplitude remains constant.
Characteristics
Better noise immunity than ASK
Requires larger bandwidth
Simple and reliable digital transmission
2. M-ary Frequency Shift Keying (M-ary FSK)
In M-ary FSK, a group of bits is transmitted as one symbol.
Bits per symbol =
Each symbol is assigned a unique carrier frequency
Example: 16-ary FSK
Bits per symbol =
Total possible 4-bit combinations = 16
Therefore, 16 different carrier frequencies are required
This improves data rate, but increases bandwidth requirement and system complexity.
Coherent and Non-Coherent FSK
Coherent FSK
Frequencies are generated from a single carrier source
Receiver requires phase synchronization
Better performance
More complex receiver design
Non-Coherent FSK
Multiple carrier sources with different frequencies are used
Phase synchronization is not required
Simpler receiver
Slightly poorer performance
Block Diagram of Frequency Shift Keying (FSK)
The FSK system consists of two main parts:
FSK Modulator (Transmitter)
FSK Demodulator (Receiver)
FSK Modulator (Transmitter)
Analog Message → ADC
The analog message signal is first converted into a digital signal using an Analog-to-Digital Converter (ADC).
Digital Message Signal
The output of the ADC is a digital signal consisting of logic 1s and logic 0s.
Carrier Signal Generation
Two carrier signals are generated:
→ carrier for logic 1
→ carrier for logic 0
NOT Gate Operation
The digital signal is split into two paths:
One path goes directly to the first multiplier
The second path passes through a NOT gate and goes to the second multiplier
Multipliers (Modulation Process)
When the digital input is logic 1:
The first multiplier is active
Carrier with frequency appears at the output
The second multiplier output is zero
When the digital input is logic 0:
The NOT gate output becomes logic 1
The second multiplier is active
Carrier with frequency appears at the output
The first multiplier output is zero
Adder
The outputs of both multipliers are added together to form the FSK signal:
(Only one frequency is present at a time.)
Band-Pass Filter (BPF)
Due to abrupt frequency switching, the signal contains unwanted frequency components.
The Band-Pass Filter:
Limits the bandwidth
Removes unwanted spectral components
Output
The filtered signal is the FSK modulated wave, ready for transmission.
FSK Demodulator (Receiver)
Received FSK Signal
The FSK modulated signal is received from the communication channel.
Multipliers (Coherent Detection)
The received signal is fed into two multipliers:
One multiplier uses carrier frequency
The other multiplier uses carrier frequency
Band-Pass Filters
BPF₁ passes only frequency
BPF₂ passes only frequency
Comparator
The outputs of the two BPFs are compared:
If output of BPF₁ > BPF₂ → logic 1
If output of BPF₂ > BPF₁ → logic 0
Recovered Digital Signal
The comparator output is a digital signal identical to the transmitted data.
Digital-to-Analog Converter (DAC)
If required, the recovered digital signal is converted back into an analog signal using a DAC.
Phase Shift Keying (PSK)
Phase Shift Keying (PSK) is a digital modulation technique in which the phase of a high-frequency carrier wave is changed (shifted) according to the digital message signal, while the amplitude and frequency of the carrier remain constant.
Each digital symbol is represented by a distinct phase angle of the carrier wave.
Basic Principle of PSK
Digital data consists of bits or groups of bits
Each symbol is assigned a fixed phase shift
Information is transmitted by changing the phase of the carrier
Amplitude and frequency do not vary
The general PSK signal is:
where
= constant amplitude
= carrier frequency
= phase corresponding to the symbol
Types of Phase Shift Keying
PSK is mainly classified into two types:
Binary Phase Shift Keying (BPSK)
M-ary Phase Shift Keying (M-ary PSK)
1. Binary Phase Shift Keying (BPSK)
In Binary PSK, one bit is transmitted at a time using two different phase angles.
Logic 1 → phase shift (for example, 90° or 180°)
Logic 0 → different phase shift (for example, 0°)
A common practical form is:
0° for logic 1
180° for logic 0
Characteristics
Very good noise immunity
Constant amplitude
Simple and reliable digital transmission
2. M-ary Phase Shift Keying (M-ary PSK)
In M-ary PSK, multiple bits are grouped together and transmitted as one symbol.
Bits per symbol =
Each symbol is assigned a unique phase shift
Example: 16-ary PSK
Bits per symbol =
Total possible 4-bit combinations = 16
Therefore, 16 different phase shifts are required
This increases data rate, but reduces noise margin.
Coherent and Non-Coherent PSK
Coherent PSK
All phase shifts are generated from a single carrier wave
Receiver requires accurate phase synchronization
Better performance
More complex receiver design
Non-Coherent PSK
Multiple carrier waves with different phase shifts are used
Phase synchronization is not strictly required
Simpler receiver
Lower performance compared to coherent PSK
Advantages of PSK
Excellent noise performance
Constant amplitude reduces power variation
More bandwidth-efficient than FSK
Widely used in modern digital communication systems
Disadvantages of PSK
Receiver is more complex
Requires phase synchronization (coherent PSK)
Higher-order PSK is sensitive to noise
Applications of PSK
Satellite communication
Wireless LANs
Mobile communication systems
GPS and digital broadcasting
Block Diagram of Phase Shift Keying (PSK)
A PSK system consists of two main sections:
PSK Modulator (Transmitter)
PSK Demodulator (Receiver)
PSK Modulator (Transmitter)
Analog Message → ADC
The analog message signal is first converted into a digital signal using an Analog-to-Digital Converter (ADC).
Digital Message Signal
The digital output consists of logic 1s and logic 0s.
Carrier Signal Generation
Two carrier signals of the same frequency and amplitude but with different phase shifts are generated:
→ carrier for logic 1
→ carrier for logic 0
NOT Gate Operation
The digital signal is split into two paths:
One path goes directly to the first multiplier
The other path passes through a NOT gate and then to the second multiplier
Multipliers (Phase Modulation Process)
When the digital input is logic 1:
First multiplier is active
Output becomes
Second multiplier output is zero
When the digital input is logic 0:
NOT gate output becomes logic 1
Second multiplier is active
Output becomes
First multiplier output is zero
Adder
The outputs of both multipliers are added:
(Only one phase-shifted carrier is present at a time.)
Band-Pass Filter (BPF)
Abrupt phase transitions introduce unwanted frequency components.
The Band-Pass Filter:
Restricts the bandwidth
Removes unwanted spectral components
Output
The filtered signal is the PSK modulated wave, ready for transmission.
PSK Demodulator (Receiver)
Received PSK Signal
The PSK modulated signal is received from the communication channel.
Multipliers (Coherent Detection)
The received signal is applied to two multipliers:
One uses carrier with phase
The other uses carrier with phase
Band-Pass Filters
BPF₁ passes the signal with phase
BPF₂ passes the signal with phase
Comparator
The outputs of the two BPFs are compared:
If output of BPF₁ > BPF₂ → logic 1
If output of BPF₂ > BPF₁ → logic 0
Recovered Digital Signal
The comparator output is the recovered digital message signal.
Digital-to-Analog Converter (DAC)
If required, the digital signal is converted back into an analog signal using a DAC.
Constellation Diagram of ASK, PSK, FSK
M-ary Encoding
M-ary encoding is a digital modulation technique in which more than two bits are transmitted simultaneously using a single signal symbol.
Here, M represents the number of distinct symbols used for transmission.
Each symbol carries log₂M bits
Higher value of M → more bits per symbol
Main goal: efficient utilization of bandwidth
Need for M-ary Encoding
In binary modulation:
1 symbol carries only 1 bit
In M-ary modulation:
1 symbol carries multiple bits
This helps to:
Reduce bandwidth requirement
Increase data rate
Improve spectral efficiency
Types of M-ary Digital Modulation
M-ary encoding can be applied to ASK, FSK, and PSK.
1. M-ary Amplitude Shift Keying (M-ASK)
M-ary ASK uses multiple amplitude levels of the carrier wave.
Each amplitude level represents a unique bit combination
Number of bits per symbol = log₂M
Example
For 16-ASK:
M = 16
Bits per symbol = log₂16 = 4
16 different amplitude levels are required
Each amplitude represents a unique 4-bit pattern
Characteristics
High data rate
Poor noise immunity
Used where channel noise is low
2. M-ary Frequency Shift Keying (M-FSK)
In M-ary FSK, the carrier frequency is shifted among M discrete frequencies.
Each frequency represents a unique symbol
Multiple bits are transmitted per symbol
Example
For 8-FSK:
M = 8
Bits per symbol = log₂8 = 3
8 different carrier frequencies are required
Characteristics
Better noise performance than M-ASK
Requires large bandwidth
Complex transmitter and receiver
3. M-ary Phase Shift Keying (M-PSK)
In M-ary PSK, the phase of the carrier wave is shifted to represent different symbols.
Carrier amplitude and frequency remain constant
Each phase shift represents a unique bit pattern
Example
For 16-PSK:
M = 16
Bits per symbol = log₂16 = 4
16 distinct phase angles are used
Characteristics
Better bandwidth efficiency than M-FSK
More sensitive to noise for higher M
Widely used in modern communication systems
Applications of Digital Modulation Techniques
1. Military Communication Systems
High security and accuracy required
Encryption possible with digital signals
Reliable communication in noisy environments
2. Mobile Communication Systems
Supports large number of users
High data rate and low interference
Efficient long-distance communication
3. Digital Broadcasting
Used in DAB, DVB, and T-DMB
Efficient transmission of audio, video, and data
High quality and reliable broadcasting
4. Radar Systems
Digital modulation used for pulse shaping
Accurate object detection and tracking
Used in weather monitoring, aviation, and defense
Advantages of Digital Modulation Techniques
1. High Immunity to Noise
Limited number of discrete symbols
Noise cannot easily convert one symbol into another
Improves reliability of received data
2. High Security
Digital data allows encryption
Ensures confidentiality, integrity, and authenticity
Not possible in analog modulation
3. Efficient Bandwidth Utilization
Compression reduces number of bits
M-ary modulation transmits multiple bits per symbol
Better use of available spectrum
4. High Accuracy of Data
Error detection and correction possible
Errors can be identified and corrected at receiver
5. High Capacity
Supports TDMA instead of FDMA
Many users share same frequency at different time slots
Increases system capacity
Disadvantages of Digital Modulation Techniques
1. Additional Circuitry
Requires ADC at transmitter
Requires DAC at receiver
Increases system cost and complexity
2. Synchronization Requirement
Carrier and clock synchronization needed
Requires stable oscillators at both ends
3. High Power Consumption
More power than pulse modulation techniques
Complex processing increases energy usage
Conclusion
Digital modulation techniques, especially M-ary encoding, play a crucial role in modern communication systems. They provide high noise immunity, improved security, efficient bandwidth usage, high accuracy, and large system capacity. Although they require additional
circuitry and power, the advantages far outweigh the disadvantages. Hence, digital modulation
is extensively used in military communication, mobile networks, broadcasting, radar systems, and advanced wireless technologies.
Quadrature Amplitude Modulation (QAM)
Definition:
QAM is a modulation technique that combines Amplitude Shift Keying (ASK) and Phase Shift Keying (PSK) to transmit information by varying both the amplitude and phase of a carrier signal simultaneously. It allows multiple bits to be transmitted per symbol, improving data rate and bandwidth efficiency.
Types of QAM:
Analog QAM:
Transmits two analog signals together using two carriers that are 90° out of phase.
Similar to standard AM but more efficient.
Used in analog TV and radio systems.
Digital QAM (Quantized QAM):
Encodes multiple bits per symbol using discrete amplitude and phase levels.
Common in digital communication systems such as Wi-Fi, LTE, and cable modems.
Examples: 16-QAM (4 bits/symbol), 64-QAM (6 bits/symbol), 256-QAM (8 bits/symbol), 1024-QAM (10 bits/symbol).
Advantages:
High data rate transmission (more bits per symbol).
Efficient use of bandwidth.
Better noise immunity compared to ASK alone.
Supports modern communication standards like Wi-Fi 6.
Disadvantages:
Receiver design is complex (must detect both amplitude and phase).
Requires coherent demodulation (accurate carrier phase and frequency at the receiver).
Sensitive to signal distortion; requires linear amplification for amplitude fidelity.
Applications:
Digital TV and cable modems.
Wi-Fi (802.11a/b/g/n/ac/ax), LTE and 5G cellular networks.
Radio communication and satellite links.
QAM Modulation & Demodulation – Step by Step
QAM (Quadrature Amplitude Modulation): A method to send data by changing both the amplitude and phase of a carrier. It combines ASK (amplitude change) and PSK (phase change).
Carrier signal: A high-frequency sine wave used to carry data. Denoted as or .
In-phase component (I): The part of the signal multiplied by the cosine carrier. Represents one data stream.
Quadrature component (Q): The part multiplied by the sine carrier (90° phase-shifted). Represents the second data stream.
Serial-to-Parallel (S/P) Conversion: Splits the input digital data into two separate streams so each can modulate I and Q components.
Digital-to-Analog Converter (DAC): Converts the digital data streams into analog signals.
Low Pass Filter (LPF): Filters out high-frequency components (like 2× carrier frequency) after demodulation to recover the original signal.
Modulation (Transmitter Side)
Serial-to-Parallel Conversion:
Split input bits into two streams: one for I, one for Q.
Example: 1101 → I: 11, Q: 01.
Digital-to-Analog Conversion (DAC):
Convert digital bits into analog voltages:
Product Modulation:
Multiply I by cosine carrier:
Multiply Q by sine carrier:
Summation:
Add the two signals to form the QAM signal:
Demodulation (Receiver Side)
Signal Splitting:
Split the received QAM signal into two paths: one for I, one for Q.
Mixing:
Multiply the I path by cosine →
Multiply the Q path by sine →
Low Pass Filtering (LPF):
Removes high-frequency terms (2× carrier)
Recovers original message signals:
Digital Conversion:
Convert analog signals back to digital bits using threshold detection.
Mathematical Explanation (Simple)
Transmitted Signal:
Demodulation (I component):
Demodulation (Q component):
Multiplying by the same carrier and filtering out high-frequency terms recovers I and Q signals.
3. Constellation Diagrams & Decision Boundaries
Constellation Diagram:
A 2D plot with I-axis (horizontal) and Q-axis (vertical).
Each point represents a symbol (combination of bits).
The position of the point depends on amplitude (distance from origin) and phase (angle).
4-QAM (Equivalent to QPSK)
Bits per symbol: 2 (e.g., 00, 01, 10, 11)
Points: in the I-Q plane
Decision boundaries: I-axis and Q-axis divide the plane into 4 quadrants
16-QAM
Bits per symbol: 4
Points: 16 points arranged in 4×4 grid
Decision boundaries: Lines halfway between points
Observation: Points are closer → more sensitive to noise